## Slide 1: Superpixel-based spectral classification for the detection of head and neck cancer with hyperspectral imaging
Hyunkoo Chung1 , Guolan Lu 1 , Zhiqiang Tian2, Dongsheng Wang3 , Zhuo Georgia Chen3, Baowei Fei1,2,4,5,
Quantitative BioImaging Lab (QBIL)
Department of Radiology and Imaging Sciences
1The Wallace H. Coulter Department of Biomedical Engineering,
Georgia Institute of Technology and Emory University, Atlanta, GA;
2Department of Radiology and Atlanta, GA;
3Department of Hematology and Medical Oncology, Emory University, Atlanta, GA;
4Department of Mathematics & Computer Science, Emory University, Atlanta, GA;
5Winship Cancer Institute of Emory University, Atlanta, GA

## Slide 2: Motivation-Head and Neck cancer
40,000 new cases of head and neck cancer in the US in 2015.
This malignancy affects the cavities, glands, and sinuses in the head and neck area.
  Over 90% of head and neck cancer are diagnosed as squamous cell carcinoma.

## Slide 3: Current methods of tumor detection
Early detection is important to improve survival and diagnosis
Traditional diagnosis
  Visual inspection
  A biopsy
Problems: subjective
  Difficulty choosing margin of cancer
Optical spectroscopy overcomes these limitations

## Slide 4: Optics to detect malignant lesions
Optical spectroscopy
  Detect malignant cancers using information from early biochemical and histological changes.
  Disadvantages: only a point measurement method
Solution: Hyperspectral Imaging (HSI)
  Hyperspectral imaging acquires continuous spectral bands by combining spectroscopy and imaging

## Slide 5: What is Hyperspectral imaging
Ability to capture large areas of tissue noninvasively without the use of a contrast agent – Label Free
Lu G, Fei B; Medical hyperspectral imaging: a review. J. Biomed. Opt. 0001;19(1):010901. doi:10.1117/1.JBO.19.1.010901.

## Slide 6: Purpose of this study
Using hyperspectral images, develop a new processing method to identify the region of tumor tissue in mice.
Algorithm
  Principal components
  Superpixels
  Support Vector Machine

## Slide 7: Experiments – Hyperspectral Imager
Reflectance images using Maestro in-vivo imaging system.
  300 Watt Xenon light source
  12 bit high-resolution charge-coupled device (CCD)
  Solid state liquid crystal filter
  Spectrally optimized lens.
  Use a 390 x 435 ROI around tumor
  Wavelengths 450 to 890 nm selected with 2nm increments
  Autoexposure and reflectance mode

## Slide 8: Experiments – Animal Model
A head and neck tumor xenograft model
Head and neck cancer cells (M4E) with green fluorescence protein (GFP)
11 female mice analyzed
Hyperspectral scans were acquired three weeks after tumor cell injection.
Anesthetized with 2% isoflurane in oxygen.
Mice #2

## Slide 9: Experiments – Ground Truth
GFP fluorescence images were also acquired for the evaluation of cancer cell detection
Histological slides analyzed to validate cancer diagnosis
Lu et al. Spectral-spatial classification for noninvasive cancer detection using hyperspectral imaging J. Biomed. Opt. 0001;19(10):106004. doi:10.1117/1.JBO.19.10.106004.

## Slide 10: Flow Chart
Pre-Processing
Raw Data
PCA
Superpixel
Feature 1
Feature 2
Feature N
SVM
Post Processing

## Slide 11: Preprocessing
A white reference image was acquired with a standard white reference board in the field of view.
A dark reference image was acquired with the camera shutter closed.
Reflectance(x, y, λ) = Raw(x, y, λ) − Dark(x, y, λ)
White(x, y, λ) − Dark(x, y, λ)

## Slide 12: Principal Components
Principal component analysis (PCA)
  Reduces the dimensionality
  Applied to the pre-processed data before superpixel segmentation
  Select the bands that that contain large variance in the data
    Selected 2 Principal Components
  Remove the step of manually choosing specific bands

## Slide 13: Principal Components
Principal Component 1
Principal Component 2
Principal Component 3

## Slide 14: Principal Components
Principal Component 4
Principal Component 5
Principal Component 6

## Slide 15: Superpixels (SLIC)
Superpixels algorithms combine pixels into meaning regions.
Simple linear iterative clustering (SLIC) technique.
  Modified K means search
Superpixel Segmentation applied to principal components.
Achanta et al SLIC Superpixels Compared to State-of-the-Art Superpixel Method IEEEE Pattern Analysis and Machine Intelligence 2012

## Slide 16: Superpixel Segmentation
SLIC Algorithm
1000 Superpixels
169,650 Pixels
170x decrease

## Slide 17: Support Vector Machine Classifier
11 tumor-bearing mice
A leave-one out method
10 mice for training and one for testing

## Slide 18: Results
18
 | Superpixel-PCA-SVM |  | SVM |  | PCA-SVM | 
Mice Number | Sensitivity | Specificity | Sensitivity | Specificity | Sensitivity | Specificity
1 | 0.84 | 0.91 | 0.41 | 0.73 | 0.72 | 0.82
2 | 0.99 | 0.84 | 0.77 | 0.71 | 0.90 | 0.77
3 | 0.96 | 0.85 | 0.47 | 0.73 | 0.80 | 0.78
4 | 0.69 | 0.89 | 0.30 | 0.64 | 0.65 | 0.71
5 | 0.99 | 0.77 | 0.55 | 0.72 | 0.88 | 0.72
6 | 0.99 | 0.84 | 0.79 | 0.80 | 0.95 | 0.79
7 | 1.00 | 0.91 | 0.88 | 0.75 | 0.89 | 0.75
8 | 1.00 | 0.84 | 0.64 | 0.70 | 0.94 | 0.74
9 | 0.98 | 0.72 | 0.45 | 0.64 | 0.76 | 0.69
10 | 0.81 | 0.92 | 0.60 | 0.77 | 0.78 | 0.88
11 | 0.93 | 0.84 | 0.49 | 0.71 | 0.81 | 0.78
Average | 0.93 | 0.85 | 0.58 | 0.72 | 0.83 | 0.77
Notes: The results of the PCA-superpixel-SVM based classifier is shown in this table. For the result using two principal components and superpixels, the superpixel-PCA-SVM based classifier obtained the highest sensitivity and specificity when compared with PCA-SVM and only SVM classifier. The superpixel-PCA-SVM achieved a sensitivity of 93% and a sensitivity of 85%. Furthermore, a comparison of techniques with and without superpixel and PCA is shown. The superpixel-PCA-SVM based method improved the average sensitivity by 35% and average specificity by 13% compared to the only SVM classifier. Furthermore, the addition of the superpixel step improved the average sensitivity by 10% and average specificity by 8% when compared to the PCA-SVM classifier.

## Slide 19: Results
PC1
PC2
Predicted
Ground Truth
Mice 1
Mice 2
Mice 7

## Slide 20: Reduction in Computation Time
SVM pixelwise method
  Train millions of pixels for classifier
  390 x 435 images
  450 to 890 nm wavelengths
  Training and testing: ≥ 20 hours
Superpixel PCA-SVM based classification
  2 Principal Components
  1000 superpixels
  Training: ≤ 15 minutes and testing: ≤ 1 min

## Slide 21: Conclusion
Proposed a superpixel based classification method for hyperspectral image classification
Tested the method in a heck and neck cancer animal model
PCA and superpixel methods reduces the dimensionality of the dataset
We are testing the hyperspectral imaging method in head and neck cancer surgical specimens from 32 patients.

## Slide 22: Acknowledgement
Funding Agency
  Georgia Research Alliance (GRA)
Quantitative BioImaging Laboratory (QBIL)

## Slide 23
feilab.org

## Slide 25: Superpixel Ground Truth
Original Ground Truth
Superpixel Ground Truth
Overlayed Superpixel Region